## Slide 1: ETERNUS CD10000
Introduction

## Slide 2: Content
Introduction
Technology
Technical Design

## Slide 3: Introduction
Fujitsu ETERNUS CD10000 basic functionalities
  Hyperscale, distributed Software-defined Storage
      Nearly unlimited and flexible scalability of capacity and performance
  Based on Ceph open source storage software
    Supporting access to object, file and block storage (truly unified)
    Fault tolerance and self-healing by design
  High performance through high parallelism of read and write operations
  Based on Intel Xeon PRIMERGY servers
4 to 224 PRIMERGY Servers (CPU, Memory, SSD, HDDs) and Network
Base Operating System (CentOS)
VSM (Web Console)
Ceph RADOS and Interfaces for (Object, Block and File)

## Slide 4: New Storage Appliance from Fujitsu
By offering a complete appliance with end-to-end maintenance ETERNUS CD10000 provides enterprise ready Ceph based storage solution
  With additional Utilities
    Event reporting and AIS Connect
    Log management
    Software update management
  With Fujitsu Maintenance Services
    Technical and maintenance services
    Customer-specific SLAs anywhere in the world
    Global reporting capabilities
  With Fujitsu Professional Services
    Design and support of turn-key applications
    Asset management and project management
Fujitsu Server & Storage Hardware
Ceph Storage System Software
Fujitsu Maintenance Services
Fujitsu Professional Services
Fujitsu add-on management functions

## Slide 5: Technology
Higher Levels of Scalability
CD10000 Hyperscale, Software-defined Storage

## Slide 6: CD10000 Hyperscale, S/W-defined Storage
Up to 224 connected Storage Nodes deliver up to 56 PB capacity
Host interfaces connect clients via 10 Gb Ethernet
Storage Nodes interconnect with InfiniBand
Software-defined storage based on Ceph open storage software
Fujitsu software enhancements for efficient management
ETERNUS CD10000
Object Level Interface
Block Level Interface
File Level Interface
Central Management
Ceph Storage System S/W and Fujitsu Extensions
10GbE Frontend Network
InfiniBand Backend Network
Performance Nodes
Capacity Nodes

## Slide 7: CD10000 Hyperscale, S/W-defined Storage
Fujitsu's appliance approach makes open source based storage enterprise ready
  Productive delivery of hardware and software, tested for full compatibility, optimized for performance and High Availability
  Full maintenance and support available from Fujitsu
  Service packs and upgrades for secure lifecycle management
Use Case Specific Interfaces
Cloud
Storage
Sync & Share
Archive
File Service
ETERNUS CD10000
Object Access
Block Access
File Access
Central Management
Ceph S/W and Fujitsu Extensions
10GbE Frontend Network
InfiniBand Backend Network
Performance Nodes
Capacity Nodes

## Slide 8: Architecture
General Architecture
Network Architecture

## Slide 9: General Architecture
ETERNUS CD10000 appliance consists of four main parts
  The Storage Nodes containing all the client data
  One Management Node
  40 Gb InfiniBand fabric
    Internal network
    Used to transmit data between the Storage Nodes
  1 Gb Ethernet fabric
    Internal network
    To manage the storage cluster
      All Storage Nodes, the InfiniBand switches, and the management node are connected to this fabric
All nodes and switches are delivered pre-installed (hardware and software) in one or more racks including internal cabling

## Slide 10: CD10000 Management Node
Management Node
  PRIMERGY RX300S8
    Intel Xeon CPU E5-2640V2, 2.00Ghz, 64GB memory
    4 x 900GB SAS 6G, 10K (two mirrors, (BOOT and DATA0))
    4 x 1GbE external ports
    1 x iRMC external port
    2 x 1GbE internal ports
    Usable Capacity – none, does not have Ceph OSDs.
  Provides management infrastructure for the cluster
    Virtual Storage Manager GUI and CLI
    Basking Management GUI
    Log Aggregation
    Alarm notifications
    Software management and deployment

## Slide 11: CD10000 Storage Nodes
Storage Nodes
  PRIMERGY RX300S8 basis server
    Intel Xeon CPU E5-2640V2, 2.00Ghz,128GB memory
    16 x 900GB SAS 6G, 10K
    2 x Infiniband, 2 x 10GbE, 2 x 1GbE, 1 x iRMC
  Basic – 2U height
    2 x 900GB mirrored drives for operating system
    14 x 900GB data drives, 1 x 785 GB SSD
    12.6 TB usable capacity
  Performance – 4U height
    2 x 900GB mirrored drives for operating system
    14 x 900GB data drives, 24 x 900GB data drives in JX40, 2 x 785GB SSDs
    34.2 TB usable capacity
  Capacity – 6U height
    2 x 900GB mirrored drives for operating system
    14 x 900GB data drives, 60 x 4TB 7.2k data drives in JX60, 1 x 785 GB SSD
    252.6 TB usable capacity

## Slide 12: CD10000 Network Architecture
10 GbE Customer Network = Client Network
Cluster network (private)
  InfiniBand (IB) based and used as cluster interconnect
  The addresses and names used in the cluster network are predefined and not changeable (192.168.40.0/23)
  Bonded, active-passive mode
Admin network (private)
  1 GbE
  Admin static (192.168.20.0/23)
  Admin DHCP (192.168.30.0/23) used for Storage Node installation with PXE & initial network setup
  Bonded, LACP mode
  iRMC static (192.168.10.0/23)
  iRMC DHCP (192.168.0.0/23)
Public network (customer)
  Clients with Ceph client software installed are connected to the storage cluster via the public network
iRMC
iRMC
iRMC
iRMC

## Slide 13: CD10000 Network Architecture
Redundant or Non-Redundant configurations available.
  Non-redundant configurations have a maximum of 23 storage nodes.
  Redundant configurations use two Brocade and two Mellanox switches to provide connections for 28 storage nodes.
Brocade ICX6610-48 Ethernet Switch (administrative network)
Mellanox IS5030 36-port Infiniband Switch (cluster network)

## Slide 14: Technical Design
Software Architecture
Fujitsu Added Value

## Slide 15: Software Architecture
CD10000 version – 1.0SP2-7
  Operating System for all nodes – CentOS 6.5
  Linux kernel - Linux3.10.42-1.el6.x86_64
  Ceph Firefly – 0.80.7

## Slide 16: Software Architecture
CD10000 based on the Ceph software architecture with the following main components
Cluster Monitors
<10
cluster membership
authentication
cluster state
cluster map
Topology
Authentication
Meta Data Server (MDS)
10s
for POSIX only
Namespace mgmt.
Metadata ops (open, stat, rename, …)
POSIX
meta data only
Object Storage Daemons (OSD)
10,000s
stores all data / FS-metadata
organizes all data in flexibly sized containers
Clients
with Ceph Client software installed
bulk data traffic
block or file or object

## Slide 17: Software Architecture
Ceph Client Interfaces
  CephFS currently not supported under GA

## Slide 18: Fujitsu Added Value (1)
ETERNUS CD10000 provides the Ceph / OpenStorage concept
  Open source software hardened and tuned to an optimized system
  Appliance built on enterprise class hardware (PRIMERGY, ETERNUS)
  Simple deployment and operation due to fully tested and preinstalled software and hardware
    Optimized performance / throughput
  Unified storage access via block, file, and object interfaces
  Hyper scale solution for 4 - 224 storage nodes

## Slide 19: Fujitsu Added Value (2)
Management and monitoring
  A web-based GUI and CLI for the Virtual Storage Manager (VSM) extended by Fujitsu's CD10000 CLI
  Collection and management of all relevant system log files, Ceph log files and SNMP messages on the Management Node to support central monitoring and maintenance
  SNMP integration of all CD10000 nodes and network components
  A central software repository on the Management Node for an easy upgrade of the software on the Storage Nodes
  AIS Connect
    Remote monitoring and service system for tele service purposes
Fully integrated in Fujitsu's enterprise class service processes

## Slide 20: Fujitsu Added Value (3)
ETERNUS CD10000 "out of the box" storage appliance is
  Hassle-free
  Maintained
Build open source storage yourself
Out of the box ETERNUS CD10000

incl. Support
incl. Maintenance