## Slide 1: ETERNUS CD10000
Service Utilities

## Slide 2: CD10000 Service Utilities
CD10000 Power On/Off
CD10000 Monitoring with SNMP
CD10000 Software Configuration & Update
CD10000 AIS Connect

## Slide 3: CD10000 Power On / Off
Power Switches
Power On
Power Off

## Slide 4: Powering On CD10000
(1) Management Node
  Both PSUs are cabled to the main power circuit (single or dual power feed) on the rear side
    Power Indicator lights orange on the front side of the operator panel
  Press the On/Off button
    The server is switched on, performs a system test and boots the factory installed operating system
(2) Storage Node
  Both PSUs are cabled to the main power circuit (single or dual power feed) on the rear side
    Power Indicator lights orange on the front side of the operator panel
  Press the On/Off button
    The server is switched on, performs a system test and boots the factory installed operating system
  ETERNUS JX40 and JX60 are powered on upon detection of SAS signal from the controlling Storage Node
(3) Wait about 15 minutes before starting any further actions

## Slide 5: Power Off CD10000
Management Node
  Stop all Storage Nodes gracefully
    Via VSM
      Select "Server Management" > "Manage Servers"
      Click on "Stop Servers"
      Select all servers in the "Stop Servers" window
    Via CLI
      "vsm_cli <cluster_name> stop"
    No cluster rebalancing will be performed
    Use ssh from the management node to login and shutdown the operating system of each storage node with an "init 0"
  As the last step shut down the management node gracefully with an "init 0"

## Slide 6: Node Operator Panel
Reset Button
  Pressing initiates a system reboot
Power On/Off Button
  Green LED when the server is on
  Orange LED when the server is switched off
    Standby mode with mains voltage present
  When the CD10000 is operating, pressing the On/Off button switches off the node
    Fujitsu strongly recommend to use the CD10000 utilities to shutdown a storage node for maintenance tasks
      CLI
        " vsm_cli <cluster_name> stop"
      VSM GUI
        Select "Server Management > Manage Servers"
        Click on "Stop Servers"

## Slide 7: CD10000 Monitoring with SNMP
Involved Main Components
Architecture of SNMP Monitoring

## Slide 8: Involved Main Components
SNMP management station
  The customer has to provide an SNMP capable network management software that performs the following tasks
    SNMP V2
    Poll the CD10000 Management Node
    Receive traps from the CD10000 Management Node
    Examples of management software
      ServerView Operations Manager
      HP OpenView
      Nagios
CD10000 Management Node
  Collects all internal SNMP Traps
  Forwards the traps to the customer SNMP Management Station

## Slide 9: Architecture of SNMP Monitoring
All SNMP traps within the CD10000 are sent to the Management Node
  Generated on the Storage Nodes
  Generated on the CD10000 switches
Management Node forwards these traps to the SNMP management station(s) of the customer
  Therefore ServerView agents are preinstalled and configured on these CD10000 components
CD10000 CLI / basking tools
  are available to configure
  SNMP communities
  SNMP Target
  For detailed information refer to the CD10000 User Guide

## Slide 10: CD10000 MIBS
All MIBs are available in the management node
See directory /usr/share/snmp/mibs
  /usr/share/snmp/mibs/FUJITSU-CD-MIB.mib – CD10000 specific MIB
  /usr/share/snmp/mibs/FSC-RAID-MIB.mib – ServerView RAID Manager MIB
  /usr/share/snmp/mibs/SRVMAGT-STATUS.mib – ServerView Agent MIB

## Slide 11: CD10000 Software Configuration & Update
Global Info Software Configuration & Update
Tasks of the Software Configuration & Update
Difference of Update/Upgrade Process
Global Update/Upgrade Process Flow
Handling Error of the Update Manager
Log Files of Update Manager
Update Manager CLI

## Slide 12: Introduction to S/W Configuration & Update
CD10000 update management system consists of
  A RPM software repository
  An Update Manager application
The RPM repository is located on the Management Node and accessible for all nodes in the storage cluster
The Update Manager is an application which manages the entire Update/Upgrade process
  From the start to the end including
    Software Updates provided on media are uploaded to the repository
    Software updates executed at all participating nodes
    Settings of the configuration, such as network
An Update/Upgrade process runs on one node at a time only to ensure the stability of the storage cluster as a whole
  Preinstalled and configured Puppet software is used for this purpose

## Slide 13: Tasks of the S/W Configuration & Update
On the Management Node
  The Puppet master manages from here the Puppet clients on the Storage Nodes and performs configuration
  The RPM repository management is managed by Pulp and served through HTTP
  The monitoring process "Monit" checks at intervals and restarts the Puppet master process in case it failed
  The Management Node itself is updated/upgraded by Update Manager, too
    Therefore a Puppet client application is also installed on Management Node
On the Storage Nodes
  The Puppet client application is responsible for update/upgrade of the storage nodes
    It is triggered by the puppet master from the Management Node
  The monitoring process "Monit" checks at intervals the Puppet client process and restarts it if not running

## Slide 14: Difference of Update/Upgrade Process
Update
  An Update process updates installed software and delivers an instruction with additional or changed steps to be executed
  No reboot is required
Upgrade
  This process is executing the same tasks as the "Update" process
  A reboot of the system is required
  The nodes are set into maintenance mode
    This prevents the CD10000 from executing rebalancing
  Therefore an upgrade process needs more time than an update process

## Slide 15: Global Update/Upgrade Process Flow (1)
Update Manager requires that all nodes are up, running and connected to the administration network
The tool "Pupped" is used and interprets its own manifest file
  Pupped manifests define resources and state of nodes
    This is applied during update/upgrade process to the nodes
  The file extension must be ".pp" and its location are under "/opt/fujitsu/fpm/manifests/"
  Partial manifests are provided by the update or upgrade media
    Describing just the content that has to be updated or changed
    The update or upgrade process merge all partial manifest into a single manifest
  Customer specific partials can be defined and default partials can be modified
    It is recommended to contact Fujitsu Technical Support before any changes are implemented
    Partials must be placed in an appropriate directory and must be checked that no conflicts occur during the merge

## Slide 16: Global Update/Upgrade Process Flow (2)
Default update process
  (1) Uploading provided RPM packages to repository
  (2) Updating cluster manifest partials using Update Manager (manifest partials contain defined cluster state)
  (3) Merging custom/changed manifests with Updates (this step can be omitted when there are no custom changes)
  (4) Updating the cluster using Update Manager
Default upgrade process
  (1) Uploading provided RPM packages to repository
  (2) Updating cluster manifest partials using Update Manager (manifest partials contain defined cluster state)
  (3) Merging custom/changed manifests with Updates (this step can be omitted when there are no custom changes)
  (4) Upgrading Management Node only. In case a manifests is applied the Management Node will be rebooted
  (5) Upgrading the cluster using Update Manager (only Storage Nodes)

## Slide 17: Handling Error of the Update Manager
The Update/Upgrade process will not start if
  Nodes are not available
  Update Manager reports a failure
    Update or upgrade of a Node has failed
      This can occur when a Node reports status "failed" or "timeout"
The Update Manager will validate puppet manifest with a puppet parser for syntax errors
  After generation of manifests
  Before running Update/Upgrade process
  If it fails the Update/Upgrade process will not start

## Slide 18: Log Files of Update Manager
On the storage nodes
  /var/log/puppet/
  var/log/monit
  /var/log/messages
On the management node
  /var/log/puppet/
  /var/log/monit
  /var/log/messages
  /var/log/pulp/
  /var/lib/puppet/reports/

## Slide 19: Update Manager CLI
General syntax of the Update Manager command line interface
  update-manager argument [--options]
  Invoked on the Management Node only
  Only Service user are allowed to execute this command (an account with administration capabilities, e.g. root)
Arguments for command "update-manager"
  "upload" Uploading RPM Packages to the RPM Repository
  "update_partials" Updating Default Manifest Partials
  "update" Sequentially updating Storage Nodes
  "upgrade" Load a software upgrade to the node Sequentially Upgrading and reboot the Nodes
For more and detailed information refer to the ETERNUS CD10000 User Guide, Chapter 9 "Software Configuration and Update/Upgrade System“ p. 185.

## Slide 20: Firmware Manager
Updates system board BIOS and iRMC firmware
  New BIOS and firmware rpm packages installed via Update Manager
  Cluster must be in HEALTH_OK
  Firmware updates are available via several options:
    Upgrading one hardware component
    Upgrading all firmware of the hardware in one node
    Upgrading all firmware of the hardware in cluster
    Upgrading management node
  Refer to Section 9.7 of the User Guide p. 97 for details.

## Slide 21: CD10000 AIS Connect
Embedded AIS Connect Agent
Internal Architecture of AIS Connect

## Slide 22: Embedded AIS Connect Agent
The ETERNUS CD10000 supports a direct connection to the Fujitsu AISConnect server without using further appliances
  SNMP traps of critical events are sent from the CD10000 via AISConnect
    This leads to automated tickets in the Fujitsu Call Management System
  Remote log-in to the ETERNUS CD10000 at customer site is possible
    Permission is under customer control and the rights have to be assigned
    Technical Support is allowed to perform remote diagnosis via tunneling (ssh and https is available) and to collect and receive log data
Customer systems are typically behind firewalls
  Most firewalls prevent inbound connections but allow outbound connections
Firewall
rejected
allowed
AIS Enterprise Backend
ETERNUS CD10000

## Slide 23: Internal Architecture of AIS Connect
The figure below shows the architecture of management node and the cooperation of the involved components inside
Refer to the ETERNUS CD10000 user guide for detailed information about
  Components of AIS Connect
  Configuration steps of AIS Connect
  Chapter "Service Support"