## Slide 1: ETERNUS CD10000
Log Files

## Slide 2: Content
Architecture of the Log Manager
Log file Collection
Log Viewer Kibana

## Slide 3: Architecture of the Log Manager

## Slide 4: Log file Collection (1)
Centralized log file management
  Log files from all Storage Nodes are collected in real-time and transferred to the Management Node
  CD10000 Log configuration file
    /opt/fujitsu/flogmanager/etc/flogmanager.conf
    By default, the log manager collects the following files
      /var/log/messages Logs of the operating system
      /var/log/snmpd/snmpd.log Logs of the SNMP agents
      /var/log/fcephadm/mkcephfs.log Logs of the storage cluster deployment
      /var/log/fcephadm/fcephadm.log Logs of vsm_cli and the ceph CLI
      /var/log/ceph/ceph.log Logs of the storage cluster
    Number of indices to be stored in the Elasticsearch database
      Default 30
      After reaching the set limit the oldest index is automatically removed daily
Following Fluentd agents are pre-configured
  Forwarder agents on all Storage Nodes
  Aggregator agents on the Management Node

## Slide 5: Log file Collection (2)
All messages are written into an Elasticsearch database on the management node
  All log files are collected daily to a file with prefix "elasticsearch_logs-" followed by yearmonthday
    For example /var/log/elasticsearch/elasticsearch_logs-20150130
Command for getting log files on demand (one time action)
  Specify a log file or a list of log files
    For one individual Storage Node
    Set of Storage Node
    All Storage Nodes
  gather -f "/var/log/puppet" -o "/tmp/logs" -n "storage13 storage14"
    Collect last log entries from File "puppet" on Storage Node 13 and 14
    Redirect the information to a file "logs" under the "/tmp" directory
    Creates a gnu-zipped file e.g. "gather-150130-101454.tar.gz"

## Slide 6: Log file Collection (2)
New commands for collecting debug information on demand are provided with SP2
  cd10000 support gather_debug_info [-n Node1 Node2] -o Target-directory
    Collect debug information from all or individual Storage Nodes or the Management Node
      About configured networks, LVM, several Ceph and VSM configuration files and general configuration information
      Creates a gnu-zipped file under the named target directory e.g. "gather-150130-111530.tar.gz"
  cd10000 support gather_sosreports [-n Node1 Node2] -o Target-directory
    Collect detailed debug information from all or individual Storage Nodes or the Management Node
    Typically this information can be requested by the central support for troubleshooting purposes when the information from "gather_debug_info" is not sufficient
    Creates a gnu-zipped file under the named target directory e.g. "gather-150130-113014.tar.gz"

## Slide 7: Log Viewer Kibana (1)
Viewing log files is possible with a log file viewer, e.g. Kibana
  This log viewer is compatible with Elasticsearch database
Single page web application
At the moment Kibana 3.1.2 supports the Elasticsearch database version 1.0.31) used by CD10000
  To verify the Elasticsearch version
1) At the time of publication

## Slide 8: Log Viewer Kibana (1)
Download free of charge Kibana from https://download.elasticsearch.org/kibana/kibana
  Extract archive (zip) to a local directory on your workstation
Modify the following line in the configuration file "kibana-[version]/config.js"
  Original entry in this configuration file
    "elasticsearch "http://"+window.location.hostname+":9200"
  Replace the placeholder "+window.location.hostname+" by the customer maintenance IP address of the CD10000 Management Node
    For example "elasticsearch: "http://10.88.4.211:9200"

## Slide 9: First Run of Log Viewer Kibana
Open the file 'kibana-[version]/index.html' in Firefox1) browser
  Choose hyperlink "Logstash Dashboard" in the middle of the window
1) Only Firefow is supported at the time of publication

## Slide 10: Basic Settings for Log Viewer Kibana
The "Logstash Dashboard" provides some default settings
  Open "Configure dashboard" in the top right corner
  Open the tab "Index"
  Change value in field "Index pattern" from "logstash-" to "logs-"
  Change "Timestamping" in the selection box to a reasonable interval and save the settings at the end

## Slide 11: Viewing the Log Entries (1)
The Time Filter restricts the search results to a specific time period
  This filter should be adjusted accordingly under the "Configure dashboard" icon in the top right
    The navigator "Timepicker" allows the corresponding settings

## Slide 12: Viewing the Log Entries (2)
Log information of the ETERNUS CD10000 is displayed

## Slide 13: Viewing the Log Entries (3)
Filtering and Query can be adjusted to personal preference